## Slide 1: Quantum Computing Architectures (EE274) Lecture 15
Hiu-Yung Wong
Mar. 18, 2025
hiuyung.wong@sjsu.edu, Office: ENG363
http://www.sjsu.edu/people/hiuyung.wong/index.html

## Slide 2: Outline
Silicon Qubits

## Slide 3: Spin Qubit Quantum Computer
Chapters 11 and 12 of “Quantum Computing Architecture and Hardware for Engineers: Step by Step”
This part has a lot of maths. You only need to be able to understand and derive them open-book (e.g. for assignment). But you need to understand what I am doing.

## Slide 4: DiVincenzo's criteria for QC
5 Necessary Criteria for quantum computing:
A scalable physical system with well characterized qubit (system needs to remain in the subspace of 2 level)
The ability to initialize the state of the qubits to a simple fiducial state (initialization time is important)
Long relevant decoherence times (much longer than gate time)
A "universal" set of quantum gates
A qubit-specific measurement capability (Some algorithms only works without measuring all qubits at the same time e.g. teleportation)
2 Necessary Criteria for quantum communication:
The ability to interconvert stationary and flying qubits (even one bit stationary and one bit flying)
The ability to faithfully transmit flying qubits between specified locations (without decoherence)
From the last lecture

## Slide 5: Why Silicon Spin Qubits
Quantum Error Correction is one of the most promising way to protect the qubit
Likely, need 1000 physical qubits to form a robust logical qubit
For complex quantum algorithm, thousands of logical qubit are required => millions of physical qubits
Quantum processors likely needs to integrate with classical processors
Si qubit is the most promising from the integration perspective
  Spin in electron
  Spin in nucleus
Learning outcomes: Understand why Si Qubit is promising
From the last lecture

## Slide 6: Properties of Si Spin-Qubit
28Si with no nuclear spin is used. Natural Si has 5% 29Si. (Need to purify to 800ppm)
Magnetic field: 1.4T
Temperature: 50mK
T2*=120us (without Echo)
From the last lecture

## Slide 7: Sidenote: Calculation of Zeeman Splitting (Is it a good 2-level system compared to the thermal energy?)
From the last lecture

## Slide 8: Storage of Electron Qubit

## Slide 9: Initialization
E.g. 1: Thermalization: Slow (T1)
E.g. 2:
  Magnetic field is pointing down
  Adjust quantum dot potential so that higher energy state (spin down) will tunnel to the reservoir => only lower energy state (spin up) left

## Slide 10: Initialization
E.g. 3
  Two states n = 1 and n =2
  Each has and
  Takes very long time for to decay to (T1)
  Use => (fast Rabi) => (fast decay) (solve the trade-off issue of the requirement of long T1!)

## Slide 11: Read-out: Spin to Charge Conversion
Spin sensing is difficult
B is pointing down (in plane of 2DEG)
GaAs/AlGaAs 2DEG
QPC Channel use to detect the charge in the quantum dot – 8ms (10X faster than G)
Wiki
M, R, T form the side wall barrier
P: Gate to control electron numbers
G: 2E4/s = (0.05ms)-1

## Slide 12: Read-out: Spin to Charge Conversion
Remember: B is down, so spin down has a higher energy; There is capacitive coupling between VP and QPC

## Slide 13: 1-Qubit Gate Implementation

## Slide 14: Case 2: Setup
29Si: 800ppm to enhance qubit coherence time
Use Electron Spin Resonance (ESR) (i.e. Rabi oscillation with oscillating magnetic field to control qubit)
Use Stark Effect to control Larmor Frequency (ESR frequency)
Single Electron Transistor (SET): sense electron occupancy in quantum dot
1.4T, 50mK
Reservoir
Confinement due to C
SET

## Slide 15: Case 2: Readout

## Slide 16: Case 2: Rabi Oscillation (Single qubit gate)