## Slide 1: Quantum Computing Architectures (EE274) Lecture 28
Hiu-Yung Wong
MAy 8, 2025
hiuyung.wong@sjsu.edu, Office: ENG363
http://www.sjsu.edu/people/hiuyung.wong/index.html

## Slide 2: Outline
Trapped Ion Qubits

## Slide 3: Fall 2025: EE 225 Introduction to Quantum Computing
(Prerequisites Graduate Students or Instructor Consent, undergraduate students are welcome!!)
A pedestrian guide on:
  Quantum Gates and Circuits
  Quantum Computing Algorithms
  Quantum Programming
  Run your program on real quantum computer (IBM-Q)
New Specialization in EE Master Degree:
Quantum Computing and Information (any 3)
This class (EE225)
EE226 Cryogenic Electronics
EE222 Advanced Integrated Devices
EE274 Quantum Computing Architectures
Email: hiuyung.wong@sjsu.edu
Video from previous classes

## Slide 4: Trapped Ions
Atomic Physics, Foot

## Slide 5: DiVincenzo's criteria for QC
5 Necessary Criteria for quantum computing:
A scalable physical system with well characterized qubit (system needs to remain in the subspace of 2 level)
The ability to initialize the state of the qubits to a simple fiducial state (initialization time is important)
Long relevant decoherence times (much longer than gate time)
A "universal" set of quantum gates
A qubit-specific measurement capability (Some algorithms only works without measuring all qubits at the same time e.g. teleportation)
From the last lecture

## Slide 6: Qubit Carrier
From the last lecture

## Slide 7: Term Symbol
171Yb
1S0
1P1
Vacuum
398.91nm
369.53nm
From the last lecture

## Slide 8: Hyperfine Structure – Well-defined two-level system
171Yb
1S0
1P1
Vacuum
398.91nm
369.53nm
Ionization
2S1/2
F=1
F=0
171Yb+
2P1/2
F=1
F=0
171Yb+
2P1/2
F=1
F=0
F=1
F=0
Qubit States
From the last lecture

## Slide 9: Why 171Yb+?
171: for ½ nuclear spin
+: for trapping
Has reasonable ionization energy
From the last lecture

## Slide 10: Ion Trapping
Atomic Physics, Foot
Linear Paul Trap
From the last lecture

## Slide 11: Ion Trapping
Atomic Physics, Foot
Wiki
From the last lecture

## Slide 12: Ion Trapping and SWAP Gate
Due to full qubit connectivity, we can implement SWAP gate using classical action.
Wiki
Compared to Superconducting qubit QC e.g. IBM_Perth
From the last lecture

## Slide 13: Laser Cooling – Absorption and Emission (Left Moving Ion)
2S1/2
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
F=1
F=0
Qubit States
From the last lecture

## Slide 14: Laser Cooling – Absorption and Emission (Right Moving Ion)
2S1/2
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
F=1
F=0
Qubit States
From the last lecture

## Slide 15: Laser Cooling – Doppler Colling
From the last lecture

## Slide 16: Measurement – Fluorescent Techniques
2S1/2
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
171Yb+
2P1/2
369.53nm
F=1
F=0
F=1
F=0
Qubit States

## Slide 17: Trapped Ions: 1-Qubit and 2 Qubit Gates
Atomic Physics, Foot

## Slide 18: Matter-Light Interaction

## Slide 19: Matter-Light Interaction

## Slide 20: Matter-Light Interaction (Monochromatic Light)

## Slide 21: Matter-Light Interaction (Rabi Oscillation)

## Slide 22: Trapped Ions: 2 Qubit Gates

## Slide 23: 2-qubit gate, Controlled-Z gate (to build: Cirac–Zoller controlled-NOT gate)

## Slide 24: 2-qubit gate, Controlled-Z gate (to build: Cirac–Zoller controlled-NOT gate)

## Slide 25: 2-qubit gate, Controlled-Z gate (to build: Cirac–Zoller controlled-NOT gate)

## Slide 26: 2-qubit gate, Controlled-Z gate (to build: Cirac–Zoller controlled-NOT gate)